Peter Tittmann

# Methods
# Results
## Treatment System Production and Cost Estimates
Time and motion, combined with production (acres treated, volume harvested), and equipment costs collected during this study will provide useful information to land managers evaluating strategies for timber harvesting and fuels reduction. In analyzing system productivity and cost, it is important to be able to differentiate the effects of machine capability from the effects of the operating conditions. For each piece of equipment we calculated operating costs based on input from equipment from vendors relevant to each piece of equipment (sale price, rated horsepower, etc.). We assumed some costs are not unique to individual pieces of equipment such as labor and fuel costs.
### Preliminary Data
We requested general equipment data equipment data from HFRD demonstration participants.
1. Caterpillar 299D XHP
  1. Cat High Flow Compact Track Loader for use in high demand applications. This is a steel track machine (optional) vs rubber belt. Also included is a HM415B designed specificially for the host machine.
2. Fecon FTX128
  1. Steel tracked forestry mulcher
3. Takeuchi TB290CL
  1. Takeuchi TB290 excavator with cab and roadliner track, manual pin-grabber coupler, FAE DML/HY-100 VT mastication head.
1. Takeuchi TL12CRH
  1. Takeuchi TL12 high flow track loader with FAE UML/SSL/VT-150 mastication head, with tooth type C/3 (standard).
    1. TL12 with ROPS/FOPS Cab with air conditioning/Heat
    2. Defroster
    3. 17.7" rubber tracks
    4. hydraulic quick attach
    5. roll up Lexan door
    6. High Flow Auxiliary Hydraulics w/second auxiliary line.
    7. FAE UML/SSL/VT-150 Universal forestry mulcher for skid steer with push-frame.
2. FAE - Prime Tech PT-175
  1. Prime Tech PT-175 Dedicated Carrier with FAE 140/U/ST-175 Mulching head with C-type teeth.
    1. Mechanical push-frame with guide pins for 140/U-175
    2. Rear winch with 5.6 t pulling power
    3. Rear view camera, with extra display
    4. Comfort driver's seat (heated and with pneumatic suspension)
    5. Reversible fan for the engine radiator (including compressor)
    6. Additional handle for emergency exit (to open it up from the outside)
    7. All cab windows in 12mm Lexan Margard.
    8. Rock guards for lower rollers.
    9. STD-500 mm tracks-single grouser
3. Kaiser S2-2
  1. Mobile walking excavator, machine works on steep slopes ranging from 30-60 degrees.
4. John Deere/Fecon JD210 with BH80EXC
  1. Crawler excavator 20 ton class with severe duty masticating head
5. 2000 Timbco Feller Buncher 425D
  1. Tracked feller buncher, FAE UMM/EX 125 mastication attachment.
Mfg	Model	Base Cost	Attch. Cost	Misc.	Total
Fecon	FTX128	$200000.0	$0.0	$0.0	0.0
Kaiser	S2-2	$350000.0	$24000.0	$0.0	24000.0
FAE - Prime Tech	PT-175	$255000.0	$0.0	$0.0	0.0
Takeuchi	TL12CRH	$86500.0	$31556.0	$0.0	31556.0
Caterpillar	299D XHP	$111000.0	$32500.0	$700.0	33200.0
Takeuchi	TB290CL	$113500.0	$23249.0	$1200.0	24449.0
John Deere/Fecon	JD210 with BH80EXC	$210000.0	$50000.0	$10000.0	60000.0
2000 Timbco Feller Buncher	425D	$450000.0	$50000.0	$5000.0	55000.0

Manufacturer	Model	Rated HP	Lubricant Res. (Gal)
Fecon	FTX128	128.0	4.0
Kaiser	S2-2	156.0	1.0
FAE - Prime Tech	PT-175	160.0	3.04
Takeuchi	TL12CRH	110.0	3.4
Caterpillar	299D XHP	106.0	3.5
Takeuchi	TB290CL	69.0	2.5
John Deere/Fecon	JD210 with BH80EXC	159.0	6.875
2000 Timbco Feller Buncher	425D	265.0	5.0

Manufacturer	Model	Rated HP	Lubricant Res. (Gal)
Fecon	FTX128	128.0	4.0
Kaiser	S2-2	156.0	1.0
FAE - Prime Tech	PT-175	160.0	3.04
Takeuchi	TL12CRH	110.0	3.4
Caterpillar	299D XHP	106.0	3.5
Takeuchi	TB290CL	69.0	2.5
John Deere/Fecon	JD210 with BH80EXC	159.0	6.875
2000 Timbco Feller Buncher	425D	265.0	5.0